## Slide 1
Connect and fetch initial data from DB
Initialise slave
Start server
Monitor for changes in DB
Monitor for changes in register (Server)
Change
[Yes]
Make changes to the register
[No]
Change
[Yes]
Make changes to the DB
Slave.py
[No]

## Slide 2
Connect and fetch initial data from DB
Initialise slave
Start server
Monitor for changes in DB
Monitor for changes in register (Server)
Change
[Yes]
Make changes to the register
[No]
Change
[Yes]
Make changes to the DB
Slave.py
[No]
def main():
conn = establish_connection()
register_values = fetch_ied_data(conn)
start_server_and_monitor(register_values)
conn.close()
if __name__ == '__main__':
main()
def establish_connection():
conn = mysql.connector.connect(
# Address of database
host="192.168.192.1",
user="root",
password="password",
database="pandapower_db"
)
return conn
def fetch_ied_data(conn):
cursor = conn.cursor()
cursor.execute("SELECT value FROM bus_voltage WHERE name='bus_voltage_0'")
voltage = int(cursor.fetchone()[0] * 1000)
cursor.execute("SELECT value FROM line_current WHERE name='line_current_0'")
current = int(cursor.fetchone()[0] * 1000)
cursor.execute("SELECT value FROM line_cb WHERE name='line_cb_0'")
breaker = int(cursor.fetchone()[0])
return [voltage, current, breaker]

## Slide 3
Connect and fetch initial data from DB
Initialise slave
Start server
Monitor for changes in DB
Monitor for changes in register (Server)
Change
[Yes]
Make changes to the register
[No]
Change
[Yes]
Make changes to the DB
Slave.py
[No]
def start_server_and_monitor(register_values):
print("|| Starting server for PLC to request for data ||")
block = ModbusSequentialDataBlock(MODBUS_DATA_ADDRESS, [0]*1100)
store = ModbusSlaveContext(hr=block)
for i in range(3):
store.setValues(FUNC_NUM, MODBUS_DATA_ADDRESS, [register_values[i]])
context = ModbusServerContext(slaves=store, single=True)
# To identify the IED
identity = create_identity()
threading.Thread(target=poll_database_and_update, args=(context,), daemon=True).start()
threading.Thread(target=monitor_modbus, args=(context,), daemon=True).start()
# Start server
StartTcpServer(
context=context,
identity=identity,
address=("0.0.0.0", 5020),
)

## Slide 4
Connect and fetch initial data from DB
Initialise slave
Start server
Monitor for changes in DB
Monitor for changes in register (Server)
Change
[Yes]
Make changes to the register
[No]
Change
[Yes]
Make changes to the DB
Slave.py
[No]
threading.Thread(target=poll_database_and_update, args=(context,), daemon=True).start()
threading.Thread(target=monitor_modbus, args=(context,), daemon=True).start()
for i in range(3):
if new_values[i] != prev_values[i]:
modbus_addr = MODBUS_DATA_ADDRESS + i context[0].setValues(FUNC_NUM, modbus_addr, [new_values[i]])
if current_value != prev_value:
write_breaker_to_db(current_value)

## Slide 5
Connect and fetch initial data from DB
Initialise slave
Start server
Monitor for changes in DB
Monitor for changes in register (Server)
Change
[Yes]
Make changes to the register
[No]
Change
[Yes]
Make changes to the DB
Slave.py
[No]

## Slide 6
Connect and query initial data from slave server
Carry out PLA logic on data
[True]
Condition
Send command to server to change register value
Client.py
[False]
Query data from slave server

## Slide 7
Connect and query initial data from slave server
Carry out PLA logic on data
[True]
Condition
Send command to server to change register value
Client.py
[False]
Query data from slave server
def establish_connection():
address = '127.0.0.1'
port_num = 5020
client = ModbusTcpClient(address, port=port_num)
client.connect()
return client
def main():
client = establish_connection()
timer_counter = 0
ls_timer_started = False
last_check_time = time.time()
while True:
register_values = fetch_register_values(client)
timer_counter, ls_timer_started, last_check_time = do_pla_logic(
client,
register_values,
timer_counter,
ls_timer_started,
last_check_time
)
time.sleep(0.5)
def fetch_register_values(client):
count = 3
rr = client.read_holding_registers(START_ADDR, count=count)
assert(rr.function_code < 0x80) # test that we are not an error
return rr.registers

## Slide 8
def do_pla_logic(client, register_values, timer_counter, ls_timer_started, last_check_time):
### LOAD SHEDDING ###
[bus_voltage_0, current_0, line_cb_0] = register_values
if less_than(bus_voltage_0/1000, TRIP_VALUE):
if not ls_timer_started:
ls_timer_started = True
last_check_time = time.time()
else:
ls_timer_started = False
timer_counter = 0
# Undervoltage
if ls_timer_started:
# Each time 1 second has passed under low-voltage condition.
# print(time.time() - last_check_time)
if time.time() - last_check_time >= 1:
timer_counter += 1
last_check_time = time.time()
print(f"[Timer] Undervoltage persists for {timer_counter} seconds")
if timer_counter == 5:
print(">> Opening line_cb_1")
if timer_counter == 15:
print(">> Opening line_cb_0")
client.write_register(START_ADDR + 2, 1)
return timer_counter, ls_timer_started, last_check_time
Connect and query initial data from slave server
Carry out PLA logic on data
[True]
Condition
Send command to server to change register value
Client.py
[False]
Query data from slave server

## Slide 9
Connect and query initial data from slave server
Carry out PLA logic on data
[True]
Condition
Send command to server to change register value
Client.py
[False]
Query data from slave server
def main():
client = establish_connection()
timer_counter = 0
ls_timer_started = False
last_check_time = time.time()
while True:
register_values = fetch_register_values(client)
timer_counter, ls_timer_started, last_check_time = do_pla_logic(
client,
register_values,
timer_counter,
ls_timer_started,
last_check_time
)
time.sleep(0.5)

## Slide 10
Connect and query initial data from slave server
Carry out PLA logic on data
[True]
Condition
Send command to server to change register value
Client.py
[False]
Query data from slave server

## Slide 11
import time
from pymodbus.client import ModbusTcpClient
#Supposed to be 0.890, but using 1 to test since bus_voltage_0 is 0.993865 which is more than 0.890 and won't trigger undervoltage
TRIP_VALUE = 1
START_ADDR = 1024
def fetch_register_values(client):
count = 3
rr = client.read_holding_registers(START_ADDR, count=count)
assert(rr.function_code < 0x80) # test that we are not an error
return rr.registers
def less_than(x, y):
return x < y
def do_pla_logic(client, register_values, timer_counter, ls_timer_started, last_check_time):
### LOAD SHEDDING ###
[bus_voltage_0, current_0, line_cb_0] = register_values
if less_than(bus_voltage_0/1000, TRIP_VALUE):
if not ls_timer_started:
ls_timer_started = True
last_check_time = time.time()
else:
ls_timer_started = False
timer_counter = 0
# Undervoltage
if ls_timer_started:
# Each time 1 second has passed under low-voltage condition.
# print(time.time() - last_check_time)
if time.time() - last_check_time >= 1:
timer_counter += 1
last_check_time = time.time()
print(f"[Timer] Undervoltage persists for {timer_counter} seconds")
if timer_counter == 5:
print(">> Opening line_cb_1")
if timer_counter == 15:
print(">> Opening line_cb_0")
client.write_register(START_ADDR + 2, 1)
return timer_counter, ls_timer_started, last_check_time
def establish_connection():
address = '127.0.0.1'
port_num = 5020
client = ModbusTcpClient(address, port=port_num)
client.connect()
return client
def main():
client = establish_connection()
timer_counter = 0
ls_timer_started = False
last_check_time = time.time()
while True:
register_values = fetch_register_values(client)
timer_counter, ls_timer_started, last_check_time = do_pla_logic(
client,
register_values,
timer_counter,
ls_timer_started,
last_check_time
)
time.sleep(0.5)
client.close()
if __name__ == '__main__':
main()